### External Rotation (ER) Sling

Indications:

For protocols involving immobilization in external rotation:  Glenohumeral dislocation/subluxation, capsular shifts, use after posterior shoulder stabilization, post-operative Bankhart procedures, soft tissue strain or repair, post-operative positioning after release of severe anterior capsule contracture.

## Step 1

- Unfasten the velcro straps at the forearm and wrist positions on the outside of the sling.

- Insert the arm into the sling, resting the cushion on your hip.  Place your arm as far back as possible in the sling and the thumb strap between the thumb and first finger.

- Reattach both the forearm and wrist straps on top of the sling to secure the arm.

## Step 2

Align cushion on the injured side at waist level with the ball (front) away from you body.  Place the pillow so the line on the top of the pillow is parallel to the front of your body.  (If you stand at a table, the line should be parallel to the table.)

### Step 3

- Bring the waist strap around from the back of the cushion around your waist, inserting into and attaching to the front buckle.

- Adjust the waist strap for proper fit.

## Step 4

Unfasten the shoulder strap buckle at the front of the cushion.  Using your free arm, reach behind your body and slip your arm through the shoulder strap.  This motion will be similar to putting on a backpack, with the wide strap fasten on the clavicular area and the thin pad in the underarm area.

NSTRUCCIONES DE COLOCACIÓN

# Text boxes

Position the white line parallel to the front of the body for indicated external rotation.

# Top view

# Rear view

## Step 6

Adjust all straps for adequate stabilization of the injured shoulder.

Put on de-rotational strap like a backpack

## Step 5

Reattach the shoulder strap to the buckle at the front of the cushion.